| Overview | This standard involves the carrying out of non-intrusive archaeological field investigations (primarily various types of survey). The standard is for archaeologists with responsibility for carrying out field investigations, i.e. they will be the most senior archaeologist in the field. They may report to a project manager or, in the case of small projects, they may be the project manager. This standard deals with the preparation for an investigation where the method statement has already been agreed, the observation and recording of measurements in the field leading to the analysis and presentation of the data. |
| --- | --- |

| Performance criteria You must be able to: | Prepare for operations 1. Verify the investigation method statement with interested parties prior to commencement 2. Identify and apply relevant technical and ethical standards 2. Confirm relevant permissions have been obtained before commencement 3. Verify relevant insurances as valid and sufficient for planned activities 4. Ensure that site facilities are appropriately located, sufficient for planned operations and fit for purpose 5. Bring suitable equipment to site and make safe and secure 6. Check measuring and recording equipment and, where required, calibrate accurately prior to use 7. Brief personnel assisting in the investigation clearly and accurately on their role, investigation methods, the site, the equipment and safety arrangements 8 Provide third parties who will be affected by the conduct of the investigation with clear and accurate information and obtain their co- operation 9 Check that safety arrangements including, signing, personal protection and access equipment comply with legislation and regulations Observe and record measurements 10. Conduct the investigation efficiently and systematically and in accordance with the method statement 11. Adapt work procedures and practices appropriately to allow for different circumstances and conditions 12. Maintain the integrity of the site, observing safe working practices and ensuring disruption to other activities on the site is kept to a minimum 13. Ensure observations and measurements are accurate and fully meet specified data requirements 14. Consult expert advice in instances where additional, specialist information is required which is relevant to the investigation 15. Advise interested parties promptly of potentially critical findings and constraints arising during the conduct of the investigation 16. Identify and recording features of the site which may require more detailed investigation 17. Ensure that investigation data are recorded clearly and accurately and are stored securely for later analysis 18. Keep a clear and accurate record of time spent on the investigation and of any problems arising during its course that may bear on either cost or accuracy 19. Maintain effective working relationships and ensuring that the project team is kept fully informed of progress and significant developments 20. Maintain equipment in operational order and storing it securely Analyse and present investigation data 21. Verify that data collected during investigation is sufficient for analytical purposes and is collated accurately 22. Check and verify investigation data for accuracy and integrity 23. Process investigation data accurately and present it in a format that will assist in making a balanced interpretation 24. Seek additional data and specialist advice where essential for accurate analysis and interpret investigation findings 25. Ensure that data outputs and supporting information comply with the requirements of the method statement, are accurate and are presented clearly in an agreed format, suitable for those who will wish to use them 26. Prepare report containing interpretation, diagnosis and advice, based on data outputs, to interested parties |
| --- | --- |

| Knowledge and understanding You need to know and understand: | 1. How to verify the aims and goals of the project 2. How to verify investigation method statements 3. How to select and secure suitable equipment and spares 4. How to check and calibrate equipment 5. How to establish site facilities 6. How to brief personnel on investigation methods 7. How to check safety arrangements and working practices 8 The relevant technical and ethical standards applicable to the work 8. The different types and modes of investigation 9. The sources of permission for access 10. The types of insurance which may be needed 11. The types of equipment which may be required 12. The types of facilities requirements 13. The types of and sources of information on safety arrangements and safe working practices, legislation and regulations which may be required 14. How to conduct investigations 15. How to identify and follow safe working practices 16. How and where to obtain specialist information and advice 17. How to observe and measure accurately 18. How to adapt investigation procedures and practices to suit different conditions 19. How to record and store investigation data 20. How to maintain equipment 21. Types and modes of investigation 22. Safe working practices which apply to the conduct of investigation 23. Sources of expert advice and specialist information 24. Circumstances and conditions which can affect investigation operations 25. Data protocols used in different investigation methods 26. Types of recording format and data storage systems used 27. How to identify data sources and select and collate data 28. How to apply valid methods to verify investigation data 29. How to process, format and present investigation data suitable for end use 30. How to advise users on the interpretation of investigation 31. The different types of investigation data 32. The limitations of techniques and data 33. The different types of data analysis 34. Data presentation formats |
| --- | --- |

| Developed by |  |
| --- | --- |
| Version number |  |
| Date approved |  |
| Indicative review date |  |
| Validity |  |
| Status |  |
| Originating organisation |  |
| Original URN |  |
| Relevant occupations |  |
| Suite |  |
| Key words |  |